## Slide 1: DSAA Final Project Review
Digital Hearing Aids
Group 51

## Slide 2: Prelude

## Slide 3: The Problem
Hearing Loss
Approximately 10% of the world’s population (760 million people) suffers from some level of hearing loss
Yet only a small percentage of this statistic use a hearing aid
What is Hearing Loss?
Hearing loss is not just a technical loss of volume rather, hearing deficiency can increase sensitivity and reduce tolerance to certain sounds while diminishing sensitivity to others.
Ski-slope Hearing Loss
One of the major kind’s of hearing loss is the Ski-slope hearing loss
When a person has problems hearing high frequency sounds the hearing curve looks like a ski slope in an audiogram

## Slide 4: Problem Statement

## Slide 5
Microphone
Amplifier
Speaker
By designing the amplifier digitally, i.e. Digital Hearing Aids which convert
sound waves into numerical codes before amplifying them and which can be programmed to perform certain functions on the input audio signal like noise reduction, signal refining etc is more advantageous than an Analog aid.
Generally, a Hearing aid has 3 basic parts :
i/p
o/p
“Our goal is to implement a hearing aid system in MATLAB for ski-slope hearing loss patients which can denoise the input signal as well as rectify it according to their preferences”

## Slide 6: Implementation

## Slide 7: Flow – Chart :
Audio Input
Low-pass filter
Addition of Noise
Denoising
Frequency Shaper
Amplitude Compression
Audio Output

## Slide 8: The GUI
Made using MATLAB app designer (guide)

## Slide 9: Record Audio

## Slide 10: Low pass filter
Input signal is sent through a low pass filter of 20,000hz
Additive White Gaussian Noise is added to the signal
White Noise: A random process signal with a constant power spectral density (PSD) function is a white noise process.
AWGN is a basic noise model used in Information theory to mimic the effect of many random processes that occur in nature.

## Slide 11: Denoising
Denoising is done with the help Wavelet Toolbox
A wavelet is a mathematical function useful in digital signal processing and image compression
It has two functions 1) ddencmp( ) 2) wdencmp( )
ddencmp returns default values for denoising or compression for the critically-sampled discrete wavelet or wavelet packet transform.
wdencmp does De-noising of the audio signal

## Slide 12: Frequency Shaping
First the signal is converted into Frequency Domain using FFT
Creates the gain filter whose maximum gain will be g_max and the minimum gain will be one. The magnitude of gain function will be the concatenation of piecewise functions.
Transition Frequencies are calculated by the Transition Vector, a set of 4 values determined by an audiologist, that define the user's hearing characteristics.
For each range, the frequency shaper applies a certain gain based on the user's specific hearing loss

## Slide 13: An example Frequency shaper transfer function
Source : Digital filtering in hearing aid system for the hearing impaired - Ritwik Dhawan, P. Mahalakshmi - Published 2016

## Slide 14: Frequency Shaping – Code Snippet

## Slide 15: Amplitude Compression
Takes in an input signal and amplifies it and makes sure that the maximum power in any frequency is less than or equal to P_sat
Also had some denoising capabilities, by zeroing out very low power frequencies.
Plow is taken as 0.01

## Slide 16: Amplitude Compression (Contd.)

## Slide 17: Results & Analysis

## Slide 18: Input File Method :

## Slide 19: Result

## Slide 20: Result (Contd.)

## Slide 21: Result (Contd.)

## Slide 22: Analysis : Input vs Output

## Slide 23: Analysis : Input vs Output
[ Unfortunately we weren’t able to show any automated way of validation for our project ]

## Slide 24: References

## Slide 25: References
Digital Hearing Aid for Ski-Slope Hearing Loss : https://research.ijcaonline.org/ncesc2017/number4/ncesc2017120.pdf
Semantic Scholar : Digital filtering in hearing aid system for the hearing impaired - Ritwik Dhawan, P. Mahalakshmi - Published 2016

## Slide 26: Thank You!
Our Git Hub Repository : https://github.com/nikhilsampangi/Digital_Hearing_Aids